## Slide 1: Final Project 5381
by Mike Mehr (mike@azuresults.com)

## Slide 2: GOALS
Pass the class!
Have fun!
Oh yeah, and it should work! 
So with that in mind, …

## Slide 3: Description
The project simulates a Smart Bulb (LED) that will
  light the darkness only when someone is in the room with it, and
  only when it’s dark enough,
  providing energy efficiency and
  a good user experience (UX).
I chose to implement all Options and added a few of my own.

## Slide 4: Options implemented
Level A (common) – LDR, Onboard LED
Level B (common) - Pushbutton
Level C Option 1 – Seven-segment display
Level C Option 2 – PIR (motion) sensor
Level C Option 3 – Environmental sensor
Extra – OLED Display (too much data!)

## Slide 5: Added features
LED color depends on light level
  Compensates to keep level constant
  Brighter output for dim ambient lighting, and vice versa
Indicators (7-seg w DP)
  Digit shows the ambient light level detected
  Decimal point shows when room is occupied
Optional environmental sensor functions (temp, press, humid, alt)
  BMP sensor provides temperature, pressure, and altitude
  BME adds humidity
  Relative height feature with reference

## Slide 6: More added features
Pushbutton modes (click to change to next)
  Smart Bulb operation (required)
  Bulb is always ON (required)
  Bulb is always OFF
  Test mode – cycles system tests to verify functionality
Relative altitude feature (pressure sensor)
  Defaults to approximate altitude above sea level, but
  If calibrated to current height, will show altitude above or below that.
  OPT: Single digit shows relative building floor, with DP for negative.
  Mode change (PB press) also sets reference pressure/altitude.

## Slide 7: Hardware Design
LPC-1769 Cortex-M3 ARM board (Mouser $23.75)
Sensors: LDR, Pushbutton (class provided)
Motion sensor: PIR-01 from OSEPP.com (Fry’s $8.99)
Seven-segment display: Common-cathode red w/DP (Amazon)
Env.sensor: BMP/BME-280 from Adafruit.com (borrowed)
  BMP – temp and pressure @ $9.95
  BME has humidity too @ $19.95
OLED: Still selecting from Adafruit.com (ran out of time)

## Slide 8: Software Architecture
Tasks to sample input sensors: 5
Tasks to drive output devices: 4
One task to act as Command Interpreter (gatekeeper)
Data flows from input tasks to GK to output tasks
Message Queues are used for data and command flow
Most queues are single length with overwrite feature
  Doesn’t matter if data is dropped
Command queue is bigger and does not drop its inputs

## Slide 9: Software architecture diagram
Commands
Outputs
Data sample
PB event
Timer event
RGB LED (GPIO)
7-seg w DP (GPIO)
OLED (I2C)
Motion-to-Presence (MTP)
BMPE (SPI)
PIR (analog)
LDR (analog)
Inputs

## Slide 10: LDR – Ambient Light Sensor
ADC input from sampling task (channel: 0, period: 250ms)
Data samples sent to command queue directly
Command proc
  Maintains current level ‘ambient’ variable
  Updates trigger immediate output
    ‘brightness’ recalc
    Brightness sent as color data to LED queue (xBulbQueue)
    Also sent as coded value to 7SEG queue (xSimple7Queue)

## Slide 11: Onboard LED task
Input data: from CQ variable ‘bulb’
Queue: xBulbQueue (1,int)
Task: “LED Output” (vTaskLEDOutput)
Just displays the output to the LED driver via led2_set(color)

## Slide 12: Onboard LED Driver
Module files: led.c/led.h
Features – display 8 basic colors [3-bit RGB (0-7)]
Uses GPIO Port pins 0.22, 3.25, 3.26

## Slide 13: PIR Motion Sensor
Not the recommended unit (got one from OSEPP at Fry’s)
This unit does not retrigger, therefore we get a pulse wave during motion, not a fixed level
The ADC task provides a train of sample levels
The Edge Detector task converts the ADC samples provided into edge events, but will not detect the lack of edges
I chose to implement a “watchdog timer” to detect lack of activity
  This works like the automatic light shutoff in some public restrooms

## Slide 14: PIR sample task
Reuses ADC task from LDR (channel: 1, period: 85ms)
Generates stream of data samples sent to Edge Detector queue

## Slide 15: Environmental sensor
Either BMP-280 or BME-280 is supported (auto-configured)
Sensor is connected via the SPI bus (sensor allows either that or I2C)
Data provided (BMP-280): temperature, pressure, altitude (relative)
Data provided (BME-280): same, plus humidity
Particular sensor boards provided by AdaFruit Industries, actual sensor on the board is by Bosch
Assembly required: solder 7-pin header, connect to breadboard (LPC)

## Slide 16: SPI background
SPI is not really a full standard, just defines a signaling method
    There are four wires: SCLK, MISO, MOSI, and SSEL (also called SS or CS)
    Three wires are usually shared, but each device needs its own CS line
    There are two operational modes: Master and Slave
    Data flows both ways simultaneously*, via frames (8-16 data bits ea.)
    Programmable clock active level (CPOL) and sampling edge (CPHA)
Speeds are set by each device; the LPC will support up to PCLK/8
The devices (Slaves) each specify how their own protocol works
    Different clock speed, bit order, and mode (CPOL/CPHA) needed for each Slave
* Most devices (including BMP) don’t use 2-way communications

## Slide 17: Bosch BMP/BME-280 sensor chip (data)
Pressure/altitude:
    Range: 300-1100 hPa (equiv.to +9000 to -500m above sea level)
    Relative accuracy of +/- 0.12 hPa (equiv. to +/- 1m~=39in.)
    Temp.correction and factory trim calibration data included
Temperature range: -40 to +85 deg.C (-40 to +185 deg.F)
Chip has on-board programmable digital filters with oversampling
Three operating modes (state transition diagram in data sheet)
    Sleep
    Forced (one sample at a time)
    Normal (filtered data streaming)

## Slide 18: Bosch BMP/BME-280 sensor chip (operation)
Operates in I2C mode until SS line goes low ↓, then permanently SPI
Selects SPI mode 0 or 3 according to SCLK level when SS line ↓
Allows clocks up to 10 MHz, 8 data bits per frame, MSB first
All transfers (register read or write) are half duplex w.2 frames:
  Frame #1: Send 7 bit register number + RW bit [1(rd)/0(wr)], ignore read byte
  Frame #2 - WR: send the data byte
  Frame #2 - RD: read the byte sent by the device
Chip ID can be read from register 0xD0: BMP=0x58, BME=0x60

## Slide 19: Chip software usage
Bosch provides original library code (usage is complicated)
AdaFruit has ported a simpler version to the Arduino hobbyist world
BMP/BME-280 has many features not supported by the basic library:
    3 operating modes (sleep, normal, forced)
    An internal IIR filter (to filter out sudden changes in pressure like door slams, etc.)
    Oversampling T, P, and H for higher resolution applications
I wanted to add a delta-height feature, but this requires the extras
I found a better library from SparkFun, but ran out of time to port it
I put in the basic functions, but the data jitters around a lot

## Slide 20: Software library
Available for Arduino from Adafruit
I chose to use this and port it to the LPC’s CMSIS library
Original characteristics:
  Written in C++
  Supports forced mode (single samples) only
  Everything calls a handful of low-level functions to access SPI
Software porting process:
  Translated original file (one .CPP/.H file pair) to BMPE.C/.H, written in C
  Rewrote the handful of low-level functions to call my own SPI layer
  Wrote the SPI layer (SPI.C/.H) to call the CMSIS functions

## Slide 21: Debugging process
Debugging protocols like SPI requires extra hardware
    See if you meet timing specs, bit order, clock modes
    Know if you’re sending and receiving data to the device properly
    Basic I/O functions need to be working well
Traditional testing would use a logic analyzer or oscilloscope ($$$)
Cheaper alternatives are available: Saleae, IkaLogic, TotalPhase
    Saleae ($109-399) and IkaLogic (€69-149) provide general logic analyzer front ends+SW
    TotalPhase provides similar but specialized for protocols: I2C/SPI/USB/CAN
    Instructor had a TotalPhase Beagle ($300), so I borrowed that (Thanks, Anil!)
    Beagle DataCenter software was a free download, easy install

## Slide 22: Debugging actually
Beagle DataCenter has quirks
  SW won’t connect to the device unless it’s operating properly first and a conversation going on (it’s a bus observer)
  Can provide error info for many issues, but they are confusing as to what you might be doing wrong
I had to solve my own bugs in the basic I/O layer (SPI.C) first
After that, it did verify that things were operating properly
The hardware hookup was pretty simple but it required +5v (J2p2)
  Anil included the $30 adapter cable, I just jumpered it to the breadboard

## Slide 23: SPI Problems encountered
Initial setup of LPC parameters is critical to get debugger working
Hidden assumptions of Arduino code had to be identified
CMSIS module was straightforward, just new names for everything
Design of SPI should allow multiple devices (w.diff.parameters)
I still want to try to get the SparkFun features working (Sept.1 baby!)
C++ really is a better fit, you should try it!

## Slide 24: Links
Contact me here: mike@azuresults.com
Link to my project on Github here (code, slides, links, more):
    https://github.com/mmehr2/FinalProject5381
Datasheets for devices used:
    PIR:
    Bosch:
    Seven-segment:
    Beagle:
Feel free to use my code in your projects if you find it valuable.

## Slide 25
THANK
YOU!
For
Watching