## Slide 1: Final Project 5381
by Mike Mehr (mike@azuresults.com)

## Slide 2: GOALS
Pass the class!
Have fun!
Oh yeah, and it should work! 
Also, I want to provide some details so others can understand what I did better.
So with that in mind, …

## Slide 3: Description
The project simulates a Smart Bulb (LED) that will
  light the darkness only when someone is in the room with it, and
  only when it’s dark enough,
  providing energy efficiency and
  a good user experience (UX).
I chose to implement all Options and added a few of my own.

## Slide 4: Options implemented
Level A (common) – LDR, Onboard LED
Level B (common) - Pushbutton
Level C Option 1 – Seven-segment display
Level C Option 2 – PIR (motion) sensor
Level C Option 3 – Environmental sensor
Extra – OLED Display (too much data!)

## Slide 5: Added features
LED color depends on light level
  Compensates to keep level constant
  Brighter output for dim ambient lighting, and vice versa
Indicators (7-seg w DP)
  Digit shows the ambient light level detected (0-8)
  Decimal point shows when room is occupied
Optional environmental sensor functions (temp, press, humid, alt)
  BMP sensor provides temperature, pressure, and altitude
  BME adds humidity
  Relative height feature with reference

## Slide 6: More added features
Pushbutton modes (click to change to next)
  Smart Bulb operation (required)
  Bulb is always ON (required)
  Bulb is always OFF
  Test mode – cycles system tests to verify functionality
Relative altitude feature (pressure sensor)
  Defaults to approximate altitude above sea level, but
  If calibrated to current height, will show altitude above or below that.
  OPT: Single digit shows relative building floor, with DP for negative.
  Mode change (PB press) also sets reference pressure/altitude.

## Slide 7: Hardware Design
LPC-1769 Cortex-M3 ARM board (Mouser $23.75)
Sensors: LDR, Pushbutton (class provided)
Motion sensor: PIR-01 from OSEPP.com (Fry’s $8.99)
Seven-segment display: Common-cathode red w/DP (Amazon)
Env.sensor: BMP/BME-280 from Adafruit.com (borrowed)
  BMP – temp and pressure @ $9.95
  BME has humidity too @ $19.95
OLED: Still selecting from Adafruit.com (ran out of time)

## Slide 8: Software Architecture
Tasks to sample input sensors: 5
Tasks to drive output devices: 4
One task to act as Command Interpreter (gatekeeper)
Data flows from input tasks to GK to output tasks
Message Queues are used for data and command flow
Most queues are single length with overwrite feature
  Doesn’t matter if data is dropped
Command queue is bigger and does not drop its inputs

## Slide 9: Software architecture diagram
Commands
Outputs
Data sample
PB event
Timer event
RGB LED (GPIO)
7-seg w DP (GPIO)
OLED (I²C)
Motion-to-Presence (MTP)
BMPE (SPI)
PIR (analog)
LDR (analog)
Inputs

## Slide 10
LEVEL A

## Slide 11: LDR – Ambient Light Sensor
Simple voltage divider circuit (10kΩ pull-up, LDR to ground)
Provides input to ADC sampling task (channel: 0, period: 250ms)
Data samples sent to Command Queue directly
Command process
  Samples maintain current sample value in Ambient variable
  Changes trigger output function of CQ
    Calculates Brightness (0-8) using Ambient, Occupancy, and Mode values
    Brightness sent as color data to LED queue (xBulbQueue)
    Also sent as coded value to 7SEG queue (xSimple7Queue)

## Slide 12: ADC sampling task
Function name: vTaskADCInput
Uses pvParameters to pass a struct pointer with parameter info:
    Channel # (0-7)
    Sampling rate (msec)
    Which command to use for sending data to the Command Queue
Process:
    Reads samples using my ADC driver module for the LPC (see ADC.C/.H)
    Sampled values are sent directly to the Command Queue
Used for both LDR and PIR sensor inputs

## Slide 13: Command Queue task
Responsible for event and data processing (inputs → outputs)
Task name: “Data Concentrator”
    Func= vTaskDataConcentrator, stack=240, no params
Queue name: xCommandQueue
    Length 10, Data: struct of 2 ints (command and data), copied by value, no overwrite
Process:
    Maintains current values of sensor levels: Mode, Ambient, Occupancy, Temp, Press, Alt
    Certain events trigger calculations that send to output queues:
      Changes to Ambient, Occupancy, or Mode send output to Bulb and 7Segment queues
      Mode change also triggers altitude referencing function
      Changes to the environment vars (Temp, Press, Humid, Alt) send output to Display queue

## Slide 14: Onboard LED Display output task
Task: “LED Output” (vTaskLEDOutput, stack 120, no params.)
Queue: xBulbQueue (1, int, w.overwrite)
Input data: brightness level (0-8)
Process:
    Converts the data to bulb color range (0-7)
    Color chosen to ‘compensate’ for light level
    For example, when the level is 0 (dark), the color is 7 (white)
    Displays the output to the LED driver via led2_set(color)

## Slide 15
LEVEL B

## Slide 16: Pushbutton input
Simple DPST pushbutton
    One pole wired between Vcc and the GPIO input (P0.9), other switch pole unused.
Debouncing done in software
    Task created to generate sample levels from the input pin (0 or 1)
    Algorithm for edge detection applied to the samples (see EDGE.C/.H)
    When enough samples accumulate in the certain pattern, an edge is returned.
    Algorithm returns +1 for leading edge (0111..1), -1 for trailing (1000..0), 0 otherwise.
Leading edge events (+1) are passed directly into Command Queue
Command process:
    Change the Mode variable to its next value (Smart → On → Off → Test → Smart…)
    Trigger the calculation update, which triggers update to the output drivers (LED, 7SEG)

## Slide 17: Alternate Pushbutton debouncing
I had initially used the interrupt driver developed in class (PA#18-19)
    However, it was sensitive to switch bouncing (of course)
After reading a few articles on bouncing on the net, I chose to use a clever software algorithm for level debouncing instead (no interrupts)
    See link here: http://www.eng.utah.edu/~cs5780/debouncing.pdf
After doing that, I thought of a way to use the “watchdog timer” method to debounce the interrupt events, but I didn’t follow up on it
    When an interrupt occurs, save the level, restart the timer and ignore other interrupts
    If the level at timer expiration is the same as at start, accept the edge
    In any case then, update the level, reset to watch for interrupts again and repeat

## Slide 18
LEVEL C1

## Slide 19: Seven Segment Display Output
Driver uses 8 GPIO pins (original P2.7:0, later P1.25:18)
    Second port used to avoid J2 connector and go out on Pads (ESD drama)
Calculations done in Command Queue task on variable change
    Only done when Ambient, Occupancy, or Mode are changed
Process:
    Uses Ambient, Occupancy, and Mode to determine Coded Value
    This value is the brightness level number (0-8) modified to add 16 when the Occupancy level is 1 (ON). Adding 16 to the code makes the Decimal Point segment light up.
    If the Mode is TEST_SEQ, the data is set to -1 instead, which will activate the Test Output mode of the 7SEG task. (This feature can be entirely removed at compile time.)
    CQ task sends Coded Value to xSimple7Queue for display

## Slide 20: 7SEG Output task
Task: “7SEG Output”, vTaskSimple7Output, 120 stack, no params
Queue name: xSimple7Queue (1, int, w.overwrite)
Process:
    If data is >= 0, it is sent to the Simple7 driver (see SIMPLE7.C/.H) as a hexadecimal digit with optional DP display.
    If data is <0, Test Mode is activated.
    In Test Mode, the task cycles periodically (period: 1 sec) through display patterns.
    At each cycle, it also peeks at the input queue to check for data
      If data >= 0 is detected, Test Mode is exited.
      If data < 0, it continues to display the test patterns.
    Test patterns show the various outputs (hex font), some rotating and alternating segments (test font), and a special ASCII input feature for fun.

## Slide 21
LEVEL C2

## Slide 22: PIR Motion Sensor
PIR = Pyroelectric (or Passive) Infrared Sensor
Not the recommended unit (got one from OSEPP at Fry’s)
This unit does not retrigger, therefore we get a square wave during motion, not a fixed level. (Times are set by trimmer pots on sensor.)
Sensor also requires several seconds of time “in the dark” when powered up to calibrate itself for best operation.

## Slide 23: PIR Software
I needed two tasks to implement the occupancy feature
The ADC task provides a train of sample levels
The Edge Detector task converts the ADC samples provided into edge events sent to the Command Queue
  First leading edge will set the occupancy state to ON,
  but will not detect the lack of edges (inactivity) to shut it OFF
I implemented a “watchdog timer” to detect inactivity
  This works like the automatic light shutoff in some public restrooms
  Timer is restarted for each edge event (both leading and trailing)
  Timer expiration sends an event to the Command Queue that shuts Occ. OFF

## Slide 24: PIR sampling task
Reuses ADC sampling task from LDR (channel: 1, period: 85ms)
Generates stream of data samples sent to Command Queue
Command Queue process:
    Data is intercepted and sent to the Edge Detector queue
    No level variable is maintained for the actual PIR sensor value
    No output update is triggered for this data
    Debug output display is optionally provided (#define DBGPRINTPIR)

## Slide 25: Edge Detector task
Uses same algorithm as Pushbutton code for converting sample levels to edges (see EDGE.C/.H)
Task name: vTaskEdgeDetector (“PIR Edges”, 120 stack, params.used)
Queue name: xEdgeDetectQueue (1, int, w.overwrite)
Process:
    Each ADC level sample from the queue,
    thresholds it with hysteresis to further prevent noise,
    And passes the resulting above/below indicator into the Edge algorithm
    This returns +1 for leading edge detected, -1 for trailing, 0 for otherwise
A +1 leading edge generates an event sent to the Command Queue

## Slide 26
LEVEL C3

## Slide 27: Environmental sensor
Either BMP-280 or BME-280 is supported (auto-configured)
Sensor is connected via the SPI bus (sensor allows either that or I²C)
Data provided (BMP-280): temperature, pressure, altitude (relative)
Data provided (BME-280): same, plus humidity
Particular sensor boards provided by AdaFruit Industries, actual sensor on the board is by Bosch
Assembly required: solder 7-pin header, connect to breadboard (LPC)

## Slide 28: BMPE Input task
Provides optional software support for either BMP-280 or BME-280
Task: “BMPE Sensors” (vTaskBMPEInput, stack 240, w.params)
    Task is not created if no sensor is detected.
Process:
    Sample period: 2000 msec using Forced mode (host demand)
    Read compensated temperature, pressure, altitude, and optional humidity.
    Scale each value to an int (scale factor 100 to get 2 decimal places).
    Send each value to the Command Queue separately.
Command process:
    When the final data (Altitude) is received, it triggers output to the OLED Display queue.

## Slide 29: OLED Display output task
Originally planned to drive an Adafruit LCD multiline display via I²C
Initial version will display to the debug console using printf.
Task: “OLED Output” (vTaskOLEDOutput, 240 stack, no params)
Queue name: xDisplayQueue (1, struct of 4 floats, w.overwrite)
Process:

## Slide 30: SPI background
SPI is not really a full standard, just defines a signaling method
    There are four wires: SCLK, MISO, MOSI, and SSEL (also called SS or CS)
    Three wires are usually shared, but each device needs its own CS line
    There are two operational modes: Master and Slave
    Data flows both ways simultaneously*, via frames (8-16 data bits ea.)
    Programmable clock active level (CPOL) and sampling edge (CPHA)
Speeds are set by each device; the LPC will support up to PCLK/8
The devices (Slaves) each specify how their own protocol works
    Different clock speed, bit order, and mode (CPOL/CPHA) needed for each Slave
* Most devices (including BMP) don’t use 2-way communications

## Slide 31: Bosch BMP/BME-280 sensor chip (data)
Pressure/altitude:
    Range: 300-1100 hPa (equiv.to +9000 to -500m above sea level)
    Relative accuracy of +/- 0.12 hPa (equiv. to +/- 1m~=39in.)
    Temp.correction and factory trim calibration data included
Temperature:
    Range: -40 to +85 deg.C (-40 to +185 deg.F)
    Resolution: 0.01 deg.C
Two data transfer modes:
    Forced – single measurement made at software request
    Normal – stream of data samples generated by device parameters (requires interrupts)
    Digital filtering and high-resolution oversampling in Normal mode only

## Slide 32: Bosch BMP/BME-280 sensor chip (operation)
Interfaces w.I²C mode until SS line goes low ↓, then permanently SPI
Selects SPI mode 0 or 3 according to SCLK level when SS line ↓
Allows clocks up to 10 MHz, 8 data bits per frame, MSB first
Simple transfers (register read or write) are half duplex w.2 frames:
  Frame #1: Send 7 bit register number + RW bit [1(rd)/0(wr)], ignore read byte
  Frame #2 - WR: send the data byte, ignore the read byte
  Frame #2 - RD: send any byte, read the byte sent by the device
Chip ID can be read from register 0xD0: BMP=0x58, BME=0x60

## Slide 33: Chip software usage
Bosch provides original library code (usage is complicated)
AdaFruit has ported a simpler version to the Arduino hobbyist world
BMP/BME-280 has extra features not supported by the basic library:
    3 operating modes (sleep, normal, forced)
    An internal IIR filter (to filter out sudden changes in pressure like door slams, etc.)
    Oversampling T, P, and H for higher resolution applications
I wanted to add a height-change feature, but this requires the extras
I found a better library from SparkFun, but ran out of time to port it
I put in the basic functions, but the data is unstable

## Slide 34: Software library
Available for Arduino from Adafruit
I chose to use this and port it to use the LPC’s CMSIS library for I/O
Original library characteristics:
  Written in C++
  Supports forced mode (single samples) only
  Everything calls a handful of low-level functions to access SPI
Software porting process:
  Translated original file (one .CPP/.H file pair) to BMPE.C/.H, written in C
  Rewrote the handful of low-level functions to call my own SPI layer
  Wrote the SPI layer (SPI.C/.H) to call the CMSIS functions

## Slide 35: Debugging process
Debugging protocols like SPI requires extra hardware
    See if you meet timing specs, bit order, clock modes
    Know if you’re sending and receiving data to the device properly
    Basic I/O functions need to be working well
Traditional testing would use a logic analyzer or oscilloscope ($$$)
Cheaper alternatives are available: Saleae, IkaLogic, TotalPhase
    Saleae ($109-399) and IkaLogic (€69-149) provide general logic analyzer front ends+SW
    TotalPhase provides similar but specialized for protocols: I²C/SPI/USB/CAN
    Instructor had a TotalPhase Beagle ($300), so I borrowed that (Thanks, Anil!)
    Beagle DataCenter software was a free download, easy install

## Slide 36: Debugging actually
Beagle DataCenter has quirks
  SW won’t connect to the device unless it’s operating properly first and a conversation going on (it’s a bus observer)
  Can provide error info for many issues, but they are confusing as to what you might be doing wrong
I had to solve my own bugs in the basic I/O layer (SPI.C) first
After that, it did verify that things were operating properly
The hardware hookup was pretty simple but it required +5v (J2p2)
  Anil included the $30 adapter cable, I just jumpered it to the breadboard

## Slide 37: SPI Problems encountered
Initial setup of LPC parameters is critical to get debugger working
Hidden assumptions of Arduino code had to be identified
CMSIS module was straightforward, just new names for everything
Design of SPI should allow multiple devices (w.diff.parameters)

## Slide 38
WRAP UP

## Slide 39: Recommendations and Ruminations
I still want to get the height change feature working (Sept.1 baby!)
C++ really is a better fit, you should try it!
Git / version control has saved my life more than once during the project. Highly recommended.
Keep on having fun with electronics and making things. Go, IoT!

## Slide 40: Links
Contact me here: mike@azuresults.com
Link to my project on Github here (code, slides, links, more):
    https://github.com/mmehr2/FinalProject5381
Datasheets for devices used – see my project
Code links – see my project
Thanks for the starter .gitignore to AlbertaSat:
    https://bitbucket.org/AlbertaSat/albertasat-athena
    Open source space satellite project originally based on FreeRTOS and LPC-1769
Feel free to use my code in your projects if you find it useful.

## Slide 41
THANK
YOU!
For
Watching

## Slide 42
END
(unused slides)

## Slide 43: Onboard LED Driver
Module files: led.c/led.h
Features – display 8 basic colors [3-bit RGB (0-7)]
Uses GPIO Port pins 0.22, 3.25, 3.26