## Slide 1: Final Project 5381
by Mike Mehr (mike@azuresults.com)

## Slide 2: GOALS
Pass the class!
Have fun!
Oh yeah, and it should work! 
So with that in mind, …

## Slide 3: Description
The project simulates a Smart Bulb (LED) that will
  light the darkness only when someone is in the room with it, and
  only when it’s dark enough,
  providing energy efficiency and
  a good user experience (UX).
I chose to implement all Options and added a few of my own.

## Slide 4: Options implemented
Level A (common) – LDR, Onboard LED
Level B (common) - Pushbutton
Level C Option 1 – Seven-segment display
Level C Option 2 – PIR (motion) sensor
Level C Option 3 – Environmental sensor
Extra – OLED Display (too much data!)

## Slide 5: Added features
LED color depends on light level
  Compensates to keep level constant
  Brighter output for dim ambient lighting, and vice versa
Indicators (7-seg w DP)
  Digit shows the ambient light level detected
  Decimal point shows when room is occupied
Optional environmental sensor functions (temp, press, humid, alt)
  BMP sensor provides temperature, pressure, and altitude
  BME adds humidity
  Relative height feature with calibration

## Slide 6: More added features
Pushbutton modes (click to change to next)
  Smart Bulb operation (required)
  Bulb is always ON (required)
  Bulb is always OFF
  Test mode – cycles system tests to verify functionality
  Smart Bulb with Relative Altitude display
Relative altitude (pressure sensor)
  Defaults to approximate altitude above sea level, but
  If calibrated to current height, will show altitude above or below that.
  Single digit shows relative building floor, with DP for negative.

## Slide 7: Hardware Design
LPC-1769 Cortex-M3 ARM board (Mouser $23.75)
Sensors: LDR, Pushbutton (class provided)
Motion sensor: PIR-01 from OSEPP.com (Fry’s $8.99)
Seven-segment display: Common-cathode red w/DP (Amazon)
Env.sensor: BMP/BME-280 from Adafruit.com (borrowed)
  BMP – temp and pressure @ $9.95
  BME has humidity too @ $19.95
OLED: Still selecting from Adafruit.com

## Slide 8: Hardware Design Diagram

## Slide 9: Software Architecture
Tasks to sample input sensors: 5
Tasks to drive output devices: 4
One task to act as Command Interpreter
Data flows from input tasks to GK to output tasks
Message Queues are used for data and command flow
Most queues are single length with overwrite feature
  Doesn’t matter if data is dropped
Command queue is bigger and does not drop its inputs

## Slide 10: Software architecture diagram
Commands
Outputs
Data sample
PB event
Timer event
RGB LED (GPIO)
7-seg w DP (GPIO)
OLED (I2C)
Motion-to-Presence (MTP)
BMPE (SPI)
PIR (analog)
LDR (analog)
Inputs

## Slide 11: LDR – Ambient Light Sensor
ADC input from sampling task (channel: 0, period: 250ms)
Data samples sent to command queue directly
Command proc
  Maintains current level ‘ambient’ variable
  Updates trigger immediate output
    ‘brightness’ recalc
    Brightness sent as color data to LED queue (xBulbQueue)
    Also sent as coded value to 7SEG queue (xSimple7Queue)

## Slide 12: Onboard LED task
Input data: from CQ variable ‘bulb’
Queue: xBulbQueue (1,int)
Task: “LED Output” (vTaskLEDOutput)
Just displays the output to the LED driver via led2_set(color)

## Slide 13: Onboard LED Driver
Module files: led.c/led.h
Features – display 8 basic colors [3-bit RGB (0-7)]
Uses GPIO Port pins 0.22, 3.25, 3.26